## Slide 1: IDP L102
Ben, Boris, Bruno, Iain, Jon, Nirmay, Oscar

## Slide 2
Electrical Development:
Rails for power, ground and connected data pins for easy and modular plug in of sensors.
Modular approach means design can be changed without issues due to soldering directly.

## Slide 3
Mechanical Development:
Chassis limit of 200mm
  Easier turning in tight spaces
  Reduces chances of collisions during line follow
Single motor for block grabbing
  Reduces economic and environmental costs
  Better for weight distribution
Modular chassis
  Can modify in real world for various applications
  Initially easier for simultaneous testing
  Better height control for mounting mechanisms
Mix of MDF + Alu + Steel Chassis
  Sheet metal forming is common and proven method - easily scalable
  Standard sized materials - reduced costs
  MDF to prevent shorting electronics
Small wheels for more compact design
  Initially ran into traction issues with the wheels
  Increased precision of chassis to fix this

## Slide 4
Software development:
Used git branching
System of .cpp and .h files in a common folder
Use of symlinks to declutter the file structure, letting .ino files access the common folder without conflict
One .ino for each test / final program
Test files for motors, flipper, all sensors
Utility file to handle serial feedback, helping with debugging
*Credit to Boris for the start button code

## Slide 5: Innovative Ideas
Block flipper
  Block intake and lifting accomplished with a single motor
  Lower cost when scaling up
  Fewer software bugs
  Large horizontal tolerance to block position
Block Identification
  Accomplished with a flexure and limit switch embedded within the flipper mechanism
  Based on difference of rigidity of the blocks
  Very reliable once tuned
Wheel Encoders
  Allow precise position monitoring and closed loop feedback system
  May not be possible to integrate them in time

## Slide 6
Sources of deviation from gantt chart:
Inconsistent wheel speeds causing robot to get lost - requiring a chassis upgrade and navigation rewrites
Timing of final chassis + flipper did not leave long for integration and testing
Residential pickup took longer than planned as a result

## Slide 7
Reflecting on the first competition:
Integration of the flipper + distance sensing was behind schedule
Result was first competition not the useful dress rehearsal it could have been, only demonstrated navigation

## Slide 8: Final competition
Have successfully picked up, identified and delivered a residential block in testing
Currently having an issue with a specific right turn to the red outpost, will need to tweak the approach to it on Tuesday
Identification and delivery of both residential blocks and a return to the finishing box is a feasible outcome for Wednesday